## Slide 1: Line Angle Sensor Design

## Slide 2: Outline
System Overview
Pivot Arm and Lower Pivot
Upper Pivot

## Slide 3: System Overview
2 Nested Axes
Renishaw RM22 13 bit encoders
Mass ~ 7.4 lbs
  Reduced to 5.3 lbs
  All from rotational mass (4.4 lbs to 2.2 lbs).
Inertia about the rotational axis reduced
  33.04 lb in^2 vs 152 lb in^2
  Achieved by changing rod to PEEK.
  Investigating use of Carbon rod instead.
    Carbon will degrade in the presence of chlorine. Likely will get several test days at minimum before it becomes an issue.
    High stiffness when compared to plastic options.

## Slide 4: Lower Pivot and Arm
316 side braces, PEEK or Carbon tether arm.
Bearings are Acetal raceway with 316 balls
  Low strength and speed, but high corrosion resistance.
  Potential improvement if transitioned to ceramic bearings, but high cost.
  Bearings rated to 30 lbf static, 50 lbf dynamic.
Design preloads the pivot on arm against the passive side of the assembly.

## Slide 5: Lower Pivot and Arm
Tether Arm is attached to the pivot using a 1/8” 316 shoulder bolt cross-drilled through the pivot and the arm.
  Reliably and repeatably attach the arm and the pivot.
Similar method is used at the far end of the tether arm to attach the tether guide.

## Slide 6: Lower Pivot Joint
Each half of the pivot joint is attached to the pivot for the upper axis.
  Lightening holes present to minimize rotating mass.
Single piece manufactured from 316.
  Doweled in place with 316 dowels.
Doweled on one side

## Slide 7: Upper Pivot
Same bearing layout as lower pivot arm.
Drilled and tapped holes for attaching an aluminum anode on each side.
Center Pivot hollowed out to reduce inertia.
Anode

## Slide 8: Upper Pivot
Each side of pivot plate is doweled into place.
4 Holes for attaching to cart or boom.
  To be designed by Dillon Herbert for DOE or TBD for Manta Ray.
Mass of stationary upper pivot components is of minimal concern
  Does not contribute to the dynamic response of the sensor.

## Slide 9: Center of Mass/Buoyancy Questions
Assumptions for FBD derivation
  Steady level flight – this is suitable for tow mode operation.
  In flight operation, @ 30 degrees of elevation, CM/CB deviations will effect both yaw and pitch.
  General thrust still applies, but with control authority moving to the rudder.
  I haven’t taken a flight dynamics course, so I’m neglecting coupling, which may have a large effect.

## Slide 10: Center of Mass/Buoyancy Questions with regards to Upright vs Inverted Flight
Upright Flight
Inverted Flight
= 0 (CM/CB Collocated)
  No effect on pitch dynamics
  Inverted flight will flip the sign on the term
    Inverting net buoyancy results in keeping the same relative sign, but changing its relative effect (no 1/m scaling term)
    Switching from positive to negative net buoyancy would increase the net effect
  - H-Stab Lift
  - Wing Lift
  - Tether Force
  – percent buoyancy
  - respective lever arm

## Slide 11: Center of Mass/Buoyancy Questions with regards to Upright vs Inverted Flight
Upright Flight
Inverted Flight
If ~= 0 (CM/CM not collocated)
  Pitch dynamics are affected
  Inverted flight will flip the sign on the term
    Inverting net buoyancy results in keeping the same relative sign, but changing its relative effect (no 1/m scaling term)
    Assuming slight positive buoyancy, increases the net effect of buoyancy
  - H-Stab Lift
  - Wing Lift
  - Tether Force
  – percent buoyancy
  - respective lever arm