## Slide 1: Line Angle Sensor Design

## Slide 2: Outline
System Overview
Sensor Choice
Pivot Arm and Lower Pivot
Upper Pivot

## Slide 3: System Overview
2 Nested Axes
Renishaw RM22 13 bit encoders
Mass ~ 7.4 lbs

## Slide 4: Lower Pivot and Arm
All 316 Construction
Bearings are Acetal raceway with 316 balls
  Low strength and speed, but high corrosion resistance.
  Potential improvement if transitioned to ceramic bearings, but high cost.
  Bearings rated to 30 lbf static, 50 lbf dynamic.
Design preloads the pivot on arm against the non sensed bearing.

## Slide 5: Lower Pivot and Arm
Tether Arm is attached to the pivot using a ¼” 316 shoulder bolt cross-drilled through the pivot and the arm.
  Reliably and repeatably attach the arm and the pivot.
Similar method is used at the far end of the tether arm to attach the tether guide.

## Slide 6: Lower Pivot Joint
Each half of the pivot joint is attached attached to the pivot for the upper axis.
Single pivot manufactured from 316.
  Doweled in place with 316 dowels.
Still deciding whether to dowel on both sides or one.
  Will likely dowel on one side and let lower shaft align opposite side.